## Slide 1: Virtual Memory
A generalization of what demand paging allows
A form of memory where the system provides a useful abstraction
  A very large quantity of memory
  For each process
  All directly accessible via normal addressing
  At a speed approaching that of actual RAM
The state of the art in modern memory abstractions

## Slide 2: The Basic Concept
Give each process an address space of immense size
  Perhaps as big as your hardware’s word size allows
Allow processes to request segments within that space
Use dynamic paging and swapping to support the abstraction
The key issue is how to create the abstraction when you don’t have that much real memory

## Slide 3: The Key VM Technology: Replacement Algorithms
The goal is to have each page already in memory when a process accesses it
We can’t know ahead of time what pages will be accessed
We rely on locality of access
  In particular, to determine what pages to move out of memory and onto disk
If we make wise choices, the pages we need in memory will still be there

## Slide 4: The Basics of Page Replacement
We keep some set of all possible pages in memory
  Perhaps not all belonging to the current process
Under some circumstances, we need to replace one of them with another page that’s on disk
  E.g., when we have a page fault
Paging hardware and MMU translation allows us to choose any page for ejection to disk
Which one of them should go?

## Slide 5: The Optimal Replacement Algorithm
Replace the page that will be next referenced furthest in the future
Why is this the right page?
  It delays the next page fault as long as possible
  Fewer page faults per unit time = lower overhead
A slight problem:
  We would need an oracle to know which page this algorithm calls for
  And we don’t have one

## Slide 6: Do We Require Optimal Algorithms?
Not absolutely
What’s the consequence of the algorithm being wrong?
  We take an extra page fault that we shouldn’t have
  Which is a performance penalty, not a program correctness penalty
  Often an acceptable tradeoff
    The more often we’re right, the fewer page faults we take

## Slide 7: Approximating the Optimal
Rely on locality of reference
Note which pages have recently been used
  Perhaps with extra bits in the page tables
  Updated when the page is accessed
Use this data to predict future behavior
If locality of reference holds, the pages we accessed recently will be accessed again soon

## Slide 8: Candidate Replacement Algorithms
Random, FIFO
  These are dogs, forget ‘em
Least Frequently Used
  Sounds better, but it really isn’t
Least Recently Used
  Assert that near future will be like the recent past
  If we haven’t used a page recently, we probably won’t use it soon
  The computer science equivalent to the “unseen hand”
Can you see why? When might they be good choices?

## Slide 9: How To Evaluate Page Replacement Algorithms
We can’t predict the future, so we approximate
Which algorithm approximates best?
Based on the number of page faults each gets while executing a standard test
What should the standard test be?
  Different algorithms will behave very differently in different situations
To test replacement algorithms, you need a clear notion of what your load is like
How exactly do I go about getting that notion?

## Slide 10: Naïve LRU
Each time a page is accessed, record the time
When you need to eject a page, look at all timestamps for pages in memory
Choose the one with the oldest timestamp
Will require us to store timestamps somewhere
And to search all timestamps every time we need to eject a page

## Slide 11: True LRU Page Replacement
a
b
c
d
a
b
d
e
f
a
b
c
d
Reference stream
Page table using true LRU
frame 0
frame 1
frame 2
frame 3
a
e
d
d
c
a
b
e
!
!
!
f
a
b
c
d
!
e
!
Loads 4
Replacements 7
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 12: Maintaining Information for LRU
Can we keep it in the MMU?
  MMU notes the time whenever a page is referenced
  MMU translation must be blindingly fast
    Getting/storing time on every fetch would be very expensive
  At best they will maintain a read and a written bit per page
Can we maintain this information in software?
  Mark all pages invalid, even if they are in memory
  Take a fault first time each page is referenced, note the time
  Then mark this page valid for the rest of the time slice
  Causing page faults to reduce the number of page faults???
We need a cheap software surrogate for LRU
  No extra page faults
  Can’t scan entire list each time, since it’s big

## Slide 13: Clock Algorithms
A surrogate for LRU
Organize all pages in a circular list
MMU sets a reference bit for the page on access
Scan whenever we need another page
  For each page, ask MMU if page has been referenced
  If so, reset the reference bit in the MMU & skip this page
  If not, consider this page to be the least recently used
  Next search starts from this position, not head of list
Use position in the scan as a surrogate for age
No extra page faults, usually scan only a few pages

## Slide 14: Clock Algorithm Page Replacement
a
b
c
d
a
b
d
e
f
a
b
c
d
Reference Stream
True LRU
LRU clock
frame 0
frame 1
frame 2
frame 3
frame 0
frame 1
frame 2
frame 3
clock
pos
a
e
d
d
c
a
b
e
d
a
b
f
a
b
c
d
a
e
d
loads 4, replacements 7
a
b
c
d
!
!
!
e
f
a
b
c
d
e
Loads 4
Replacements 7
0
1
2
3
0
0
0
0
3
1
!
!
3
1
1
0
2
3
!
!
!
!
!
!
!
1
2
0
!
2
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 15: Comparing True LRU To Clock Algorithm
Same number of loads and replacements
  But didn’t replace the same pages
What, if anything, does that mean?
Both are just approximations to the optimal
If LRU clock’s decisions are 98% as good as true LRU
  And can be done for 1% of the cost (in hardware and cycles)
  It is a bargain!

## Slide 16: Page Replacement and Multiprogramming
We don’t want to clear out all the page frames on each context switch
How do we deal with sharing page frames?
Possible choices:
  Single global pool
  Fixed allocation of page frames per process
  Working set-based page frame allocations

## Slide 17: Single Global Page Frame Pool
Treat the entire set of page frames as a shared resource
Approximate LRU for the entire set
Replace whichever process’ page is LRU
Probably a mistake
  Bad interaction with round-robin scheduling
  The guy who was last in the scheduling queue will find all his pages swapped out
  And not because he isn’t using them
  When he gets in, lots of page faults

## Slide 18: Per-Process Page Frame Pools
Set aside some number of page frames for each running process
  Use an LRU approximation separately for each
How many page frames per process?
Fixed number of pages per process is bad
  Different processes exhibit different locality
    Which pages are needed changes over time
    Number of pages needed changes over time
  Much like different natural scheduling intervals
We need a dynamic customized allocation