## Slide 1: I/O Architecture
I/O is:
  Varied
  Complex
  Error prone
A bad place for the typical user to be wandering around
The operating system really needs to make I/O a lot friendlier

## Slide 2: Important Elements of I/O Architecture
Types of I/O devices
Busses
  Types, arbitration, bus-mastering
Device controllers
  Controller registers
  A sample device
  Direct I/O

## Slide 3: What Counts as an I/O Device?
Storage devices (hard drives, flash drives, DVD/CD drives, tape drives)
Displays (monitors and speakers)
Input devices (keyboards, mice, microphones and cameras)
Network devices (wired and wireless, including 802.11, Bluetooth, maybe infrared)
Sensor devices (GPS, accelerometers, etc.)
And sometimes exotic stuff

## Slide 4: Sequential vs. Random Access Devices
Sequential access devices
  Byte/block N must be read/written before byte/block N+1
  May be read/write once, or may be rewindable
  Examples: magnetic tape, printer, keyboard
Random access devices
  Possible to directly request any desired byte/block
  Getting to that byte/block may or may not be instantaneous
  Examples: memory, magnetic disk, graphics adaptor
They are used very differently
  Requiring different handling by the OS

## Slide 5: Busses
Something has to hook together the components of a computer
  The CPU, memory, various devices
Allowing data to flow between them
That is a bus
A type of communication link abstraction

## Slide 6: A Simple Bus
main bus
controller
controller
device
CPU
memory
control
address
data
interrupts

## Slide 7: Memory Type Busses
Initially back-plane memory-to-CPU interconnects
  A few “bus masters”, and many “slave devices”
  Arbitrated multi-cycle bus transactions
    Request, grant, address, respond, transfer, ack
    Operations: read, write, read/modify/write, interrupt
Originally most busses were of this sort
  ISA, EISA, PCMCIA, PCI, cPCI, video busses, ...
  Distinguished by
    Form-factor, speed, data width, hot-plug, maximum length, ...
    Bridging, self identifying, dynamic resource allocation, …

## Slide 8: Bus Masters, Slaves, and Arbitration
Bus master
  Any device (or CPU) that can request the bus
  One can also speak of the “current bus master”
Bus slave
  A device that can only respond to bus requests
Bus arbitration
  Process of deciding to whom to grant the bus
    May be based on time, geography or priority
    May also clock/choreograph steps of bus cycles
    Bus arbitrator may be part of CPU or separate

## Slide 9: Network Type Busses
Evolved as peripheral device interconnects
  SCSI, USB, 1394 (Firewire), Infiniband, ...
  Cables and connectors rather than back-planes
  Designed for easy and dynamic extensibility
  Originally slower than back-plane, but no longer
Much more like a general purpose network
  Packet switched, topology, routing, node identity
  May be master/slave (USB) or peer-to-peer (1394)
  May be implemented by controller or by host

## Slide 10: Devices and Controllers
I/O devices
  Peripheral devices that interface between the computer and other media
    Disks, tapes, networks, serial ports, keyboards, displays, pointing devices, etc.
Device controllers connect a device to a bus
  Communicate control operations to device
  Relay status information back to the bus
  Manage DMA transfers for the device
  Generate interrupts for the device
Controller usually specific to a device and a bus

## Slide 11: Device Controller Registers
Device controllers export registers to the bus
  Registers in controller can be addressed from bus
  Writing into registers controls device or sends data
  Reading from registers obtains data/status
Register access method varies with CPU type
  May use special instructions (e.g., x86 IN/OUT)
    Privileged instructions restricted to supervisor mode
  May be mapped onto bus like memory
    Accessed with normal (load/store) instructions
    I/O address space not accessible to most processes

## Slide 12: A Simple Device
16550 UART
Designed to perform asynchronous serial communications
  E.g., modems, printers, other simple devices
Often used in PCs
Allows data to be moved to/from a device a byte at a time

## Slide 13: The 16550 UART and the Bus

## Slide 14: 16550 UART Registers
0: Data – read received byte, write to transmit a byte
1: Interrupt enables – for transmit done, data received, etc.
2: Interrupt registers – currently pending interrupt conditions
3: Line control register – character length, parity and speed
4: Modem control register – control signals sent by computer
5: Line status register – transmit/receive completion and error conditions
6: Modem status registers – received modem control signals

## Slide 15: Direct Polled I/O
One way of moving data into/out of computer
  Using UART 16550, for example
All transfers happen under direct control of CPU
  CPU transfers data to/from device controller registers
  Transfers are typically one byte or word at a time
  May be accomplished with normal or I/O instructions
CPU polls device until it is ready for data transfer
  Received data is available to be read
  Previously initiated write operations are completed
Advantages
  Very easy to implement (both hardware and software)

## Slide 16: Disadvantage of Direct Polled I/O
CPU-intensive data transfers
  Each byte/word requires multiple instructions
CPU wasted while awaiting completion
  Busy-wait polling ties up CPU until I/O is completed
Devices are idle while we are running other tasks
  I/O can only happen when an I/O task is running
How can these problems be dealt with?
  Let controller transfer data without attention from CPU
  Let application block pending I/O completion
  Let controller interrupt CPU when I/O is finally done
Requires OS support

## Slide 17: Handling I/O Performance Issues
Various techniques are possible
Direct Memory Access (DMA)
  Non-CPU bus-masters
  Completion interrupts
  Typical DMA programming
Enhanced Techniques
  Memory Mapped I/O
  Smart Device Controllers
  I/O Channel Controllers

## Slide 18: Direct Memory Access
Essentially, use the bus without CPU control
  Move data between memory and device controller
Bus facilitates data flow in all directions between:
  CPU, memory, and device controllers
CPU can be the bus-master
  Initiating data transfers with memory, device controllers
But device controllers can also master the bus
  CPU instructs controller what transfer is desired
    What data to move to/from what part of memory
  Device controller does transfer w/o CPU assistance
  Device controller generates interrupt at end of transfer

## Slide 19: DMA Interrupts
CPU usually needs to know when DMA is done
Handled by sending interrupt on the bus
  Devices signal controller when they are done/ready
  When device finishes, controller puts interrupt on bus
CPUs and interrupts
  Interrupts look very much like traps
    Traps come from CPU, interrupts are caused externally
  Unlike traps, interrupts can be enabled/disabled
    A device can be told it can or cannot generate interrupts
    Special instructions can enable/disable interrupts to CPU

## Slide 20: Interrupt Handling
1st level
interrupt handler
2nd level handler
(device driver interrupt routine)
return to
user mode
Application Program
user mode
supervisor mode
PS/PC
interrupt vector table
PS/PC
PS/PC
PS/PC
instr ;
instr ;
instr ;
instr ;
instr ;
instr ;
driver
driver
driver
driver
list of device interrupt handlers
device
requests
interrupt

## Slide 21: Interrupts vs. Traps
Most traps caused by an instantaneous condition
  Triggered in response to illegal program actions
  Related to something CPU was doing
Interrupts are caused a device being in some state
  Triggered when the device enters a particular state
    E.g., device state changes from BUSY to DONE
  They are asserted as long as device is in that state
    E.g., until the device is BUSY again
Once delivered, an interrupt must be disabled
  CPU must ignore continuing request for that interrupt
  Cause must be cleared, and interrupt acknowledged

## Slide 22: Performing I/O Using Interrupts
Requesting process checks to see if device is busy
  If idle, start the I/O operation, and await its completion
  Meanwhile, CPU does something else (for this process or another one)
  If busy, wait for the device to become idle
I/O interrupt handler
  Gathers completion information from the device
  Awakes requester to handle the interrupt
When current owner finishes using the device
  Wake up the next requester
We'll talk about waiting and waking up soon

## Slide 23: Problems With DMA
DMA is designed for fairly large data transfers
What if you want to move a rather small amount of data?
  Frequently and efficiently
  E.g., consider a video game display adaptor
  Lots of data in the display, but maybe only a few bytes get updated
DMA is rather heavyweight for that

## Slide 24: Memory Mapped I/O
CPU treats control and data registers of I/O devices as if they were memory addresses
Reads/writes to them just like memory
Makes everything the processor works with look just like memory
  No special instructions to read/write I/O devices
Applications themselves can write to the memory locations
  Avoiding traps to the OS

## Slide 25: A Memory Mapping Example
A bit-mapped display adaptor
  1Mpixel display controller, on the CPU memory bus
  Each word of display memory corresponds to one pixel
  Application uses ordinary stores to update display
  Device always has access to the data without interrupts or polling
Low overhead per update, no interrupts
Relatively easy to program

## Slide 26: Memory Mapping Devices and Security
Memory mapped I/O from ordinary instructions gives user-mode processes direct access to an I/O device
Isn’t this a security problem?
  Yes, but perhaps the device does not contain anybody else’s data
    E.g., the device is a graphics adaptor and the program is a video game
  Memory mapping devices is a protected operation
  OS controls which processes can use which devices when

## Slide 27: DMA vs. Memory Mapping
DMA performs large transfers efficiently
  Better utilization of both the devices and the CPU
    Device doesn't have to wait for CPU to do transfers
  But there is considerable per transfer overhead
    Setting up the operation, processing completion interrupt
Memory-mapped I/O has no start/finish overhead
  But every byte is transferred by a CPU instruction
    No waiting because device accepts data at memory speed
DMA better for occasional large transfers
Memory-mapped better for frequent small transfers
Memory-mapped devices more difficult to share
Memory mapping can be used to set up DMA

## Slide 28: Smart Device Controllers
Smarter controllers can improve on basic DMA
They can queue multiple input/output requests
  When one finishes, automatically start next one
  Reduce completion/start-up delays
  Eliminate need for CPU to service interrupts
They can relieve CPU of other I/O responsibilities
  Request scheduling to improve performance
  They can do automatic error handling & retries
Abstract away details of underlying devices

## Slide 29: Channels – I/O Coprocessors
Channels sit between CPU and I/O devices
  Think of them as extremely smart busses
They include highly specialized CPUs
  They execute channel I/O programs
    Instructions to read, write and control devices
    Instructions to generate progress interrupts
Once started, I/O programs execute w/o CPU attention
  Command chaining, from one command to next
  Data chaining, from one buffer to next

## Slide 30: Typical Channel Architecture
main bus
channel
controller
0x2??
channel
controller
0x1??
CPU
memory
device
controller
0x10?
device 0x100
device
controller
0x1F0?
device 0x101
device 0x10F
…
…
Channels, controllers, and devices, all have assigned (relatively geographic) addresses.

## Slide 31: Busses, I/O, and Abstractions
The bus itself is an example of the communication link abstraction
  Provides read/write operations between different parts of the computer
  With lots of asynchrony, variations, and possible failures
Device controllers are examples of the interpreter abstraction
  They are specialized interpreters designed to handle special needs of I/O