## Slide 1: Disk Drives
An especially important and complex form of I/O device
Still the primary method of providing stable storage
  Storage meant to last beyond a single power cycle of the computer
A place where physics meets computer science
  Somewhat uncomfortably

## Slide 2: Some Important Disk Characteristics
Disks are random access devices (mostly . . .)
  With complex usage, performance, and scheduling
Key OS services depend on disk I/O
  Program loading, file I/O, paging
  Disk performance drives overall performance
Disk I/O operations are subject to overhead
  Higher overhead means fewer operations/second
  Careful scheduling can reduce overhead
  Clever scheduling can improve throughput, delay

## Slide 3: Disk Drives – A Physical View

## Slide 4: Disk Drives – A Logical View
cylinder
(10 corresponding tracks)
platter
surface
track
sectors

## Slide 5: Disk Drive Terms
Spindle
  A mounted assembly of circular platters
Head assembly
  Read/write head per surface, all moving in unison
Track
  Ring of data readable by one head in one position
Cylinder
  Corresponding tracks on all platters
Sector
  Logical records written within tracks
Disk address = <cylinder / head / sector >

## Slide 6: Seek Time
At any moment, the heads are over some track
  All heads move together, so all over the same track on different surfaces
If you want to read another track, you must move the heads
The time required to do that is seek time
Seek time is not constant
  Amount of time to move from one track to another depends on start and destination
  Usually reported as an average
What if each head could move independently? What would the benefits be? What complexities are added?

## Slide 7: Rotational Delay
Once you have the heads over the right track, you need to get them to the right sector
The head is over only one sector at a time
If it isn’t the right sector, you have to wait for the disk to rotate over that one
Like seek time, not a constant
  Depends on which sector you’re over
  And which sector you’re looking for
  Also usually reported as an average
Also called latency

## Slide 8: Transfer Time
Once you’re on the correct track and the head’s over the right sector, you need to transfer data
You don’t read/write an entire sector at a time
There is some delay associated with reading every byte in the sector
All sectors are usually the same size
So transfer time is usually constant

## Slide 9: Disk Drives and Controllers
The disk drive is not directly connected to the bus
It is connected to a disk drive controller
  Special hardware designed for this task
There may be several disk drives attached to the same controller
  Which then multiplexes its attention between them
Many disks have their controller bundled with them (e.g., SCSI disks)

## Slide 10: Typical Disk Drive Performance
heads | 10 |  | platters | 5
cylinders | 17,000 |  | tracks/inch | 18,000
sectors/track | 400 |  | bytes/sector | 512
RPM | 7200 |  | speed | 196Mb/sec
seek time | 0-15 ms |  | latency | 0-8ms
Time to read one 8192 byte block |  |  |  | 
 | seek | rotate | transfer | total
best case | 0ms | 0ms | 333us | 333us
worst case | 15ms | 8ms | 333us | 23.3ms (70X)
average | 9ms | 4ms | 333us | 13.3ms (40X)

## Slide 11: Why Is This Problematic For the OS?
When you go to disk, it could be fast or slow
  If you go to disk a lot, that matters
The OS can make choices that make it faster or slower
  Deciding where to put a piece of data on disk
  Deciding when to perform an I/O
  Reordering multiple I/Os to minimize seek time and latency
  Perhaps optimistically performing I/Os that haven’t been requested

## Slide 12: Optimizing Disk I/O
Don't start I/O until disk is on-cylinder or near sector
  I/O ties up the controller, locking out other operations
  Other drives seek while one drive is doing I/O
Minimize head motion
  Do all possible reads in current cylinder before moving
  Make minimum number of trips in small increments
Encourage efficient data requests
  Have lots of requests to choose from
  Encourage cylinder locality
  Encourage largest possible block sizes
  All by OS design choices, not influencing programs/users
Instead of optimizing a particular disk I/O, the OS can switch to another task and run that while waiting for the I/O. How much disk optimization should the OS do vs. how much alternate task scheduling?
The OS can also decide where a piece of data goes on the disk to begin with, and can even move data around on disk. What possibilities does that allow us?

## Slide 13: Algorithms to Control Head Movement
First come, first served
  Just do them in the order they happen
Shortest seek time first
  Always go with the request that’s closest to the current head position
  Since requests keep arriving, can cause starvation
Scan/Look (AKA the Elevator Algorithm)
  Service all requests in one direction, then go in the other direction
  No starvation, but may take longer

## Slide 14: Head Travel With Various Algorithms
Scan/Look (elevator algorithm) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
76 |  | 124 |  | 137 |  | 201 |  | 269 |  | 29 |  | 17 |  | 12
 | 48 |  | 13 |  | 64 |  | 68 |  | 240 |  | 12 |  | 5 | 
total head motion: 450 cylinders |  |  |  |  |  |  |  |  |  |  |  |  |  | 
First Come First Served |  |  |  |  |  |  |  |  |  |  |  |  |  | 
76 |  | 124 |  | 17 |  | 269 |  | 201 |  | 29 |  | 137 |  | 12
 | 48 |  | 107 |  | 252 |  | 68 |  | 172 |  | 108 |  | 125 | 
total head motion: 880 cylinders |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Shortest Seek First |  |  |  |  |  |  |  |  |  |  |  |  |  | 
76 |  | 29 |  | 17 |  | 12 |  | 124 |  | 137 |  | 201 |  | 269
 | 47 |  | 12 |  | 5 |  | 112 |  | 13 |  | 64 |  | 68 | 
total head motion: 321 cylinders |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 15: Disks as an Example of the Memory Abstraction
They support the read and write operations
But, unlike RAM, they are not word-addressable
  You read and write sectors
Also unlike RAM, they have variable delays in their operations
  Not just because of queued operations, either
Either the OS must expose these differences
  Or work to hide them
Flash memory can also provide persistent storage, with very different, but also limiting, characteristics. Writes are slower than reads, you can’t re-write without first performing a very slow erase, and you can only erase a certain number of times total. How do those characteristics change how the OS should work with flash memory vs. disks?