## Slide 1: Modularity and Memory
Clearly, programs must have access to memory
We need abstractions that give them the required access
  But with appropriate safety
What we’ve really got (typically) is RAM
RAM is pretty nice
  But it has few built-in protections
So we want an abstraction that provides RAM with safety

## Slide 2: What’s the Safety Issue?
We have multiple threads running
Each requires some memory
Modern architectures typically have one big pool of RAM
How can we share the same pool of RAM among multiple processes?
  Giving each what it needs
  Not allowing any to harm the others

## Slide 3: Domains
A simple memory abstraction
Give each process access to some range of the physical memory
  Its domain
  Different domain for each process
Allow process to read/write/execute memory in its domain
And not touch any memory outside its domain

## Slide 4: Mapping Domains
Program 1
Program 2
Program 3
Program 4
Processor
Memory
Disk
Network
Every process gets its own piece of memory
No process can interfere with other processes’ memory

## Slide 5: What Do Domains Require?
Threads will issue instructions
  Perhaps using arbitrary memory addresses
Only addresses in the thread’s domain should be honored
  Issuing any other address should be caught as an error
Can’t trust threads to police their own addresses
  System must enforce that

## Slide 6: Making It Work
Generally requires hardware support
In a simple way, a domain register
  A processor has perhaps just one
  It specifies the domain associated with the thread currently using the processor
  By listing the low and high addresses that bound the domain
OK, so we know what the thread’s domain is
Now what?

## Slide 7: The Memory Manager
Hardware or software that enforces the bounds of the domain register
When thread reads or writes an address, memory manager checks the domain register
If within bounds, do the memory operation
If not, throw an exception
Only trusted code (i.e., the OS) can change the domain register

## Slide 8: Illegal Memory Reference Exceptions
The exception that gets thrown when a thread asks for memory not in its domain
  Giving access might screw up another program
What happens then?
Trap to supervisor mode
  To handle the problem safely

## Slide 9: The Domain Register Concept
Processor
Memory
Disk
Network
Program 1
Program 4
Domain Register
All Program 1 references must be within these bounds
All Program 4 references must be within these bounds
Enforced by hardware

## Slide 10: Multiple Domains
Limiting a process to a single domain is not too convenient
The concept is easy to extend
  Simply allow multiple domains per process
Obvious way to handle this is with multiple domain registers
  One per allocated domain

## Slide 11: The Multiple Domain Concept
Program 1
Processor
Memory
Disk
Network
Domain Registers

## Slide 12: Handling Multiple Domains
Programs can request more domains
  But the OS must set them up
What does the program get to ask for?
  A specific range of addresses?
  Or a domain of a particular size?
Latter is easier
  What if requested set of addresses are already used by another program?
  Memory manager can choose a range of addresses of requested size
But what if the program is written to use a specific set of addresses?

## Slide 13: Domains and Access Permissions
One can typically do three types of things with a memory address
  Read its contents
  Write a new value to it
  Execute an instruction located there
System can provide useful effects if it does not allow all modes of use to all addresses
Typically handled on a per-domain basis
  E.g., read-only domains
Requires extra bits in domain registers
And other hardware support

## Slide 14: What If Program Uses a Domain Improperly?
E.g., it tries to write to a read-only domain
A permission error exception
  Different than an illegal memory reference exception
But also handled by a similar mechanism
Probably want it to be handled by somewhat different code in the OS
Remember discussion of trap handling in previous lecture?

## Slide 15: Do We Really Need to Switch Processes for OS Services?
When we trap or make a request for a domain, must we change processes?
  We lose context doing so
Instead, run the OS code for the process
  Which requires changing to supervisor mode
  Context for process is still available
But what about safety?
  Use domain access modes to ensure safety
We don’t do this for all OS services . . .

## Slide 16: Domains in Kernel Mode
Allow user threads to access certain privileged domains
  Such as code to handle hardware traps
  Such code must be in a domain accessible to the user thread
But can’t allow arbitrary access to those privileged domains
A supervisor (AKA kernel) mode access bit is set on such domains
  So thread only accesses them when in kernel mode

## Slide 17: How Does a Thread Get to Kernel Mode?
Can’t allow thread to arbitrarily put itself in kernel mode any time
  Since it might do something unsafe
Instead, allow entry to kernel mode only in specific ways
  In particular, only at specific instructions
  These are called gates
  Typically implemented in hardware using instruction like SVC (supervisor call)
  Remember trapping to supervisor mode?